## Slide 1: On-board Diagnostics II
OBD2 Overview

## Slide 2: On-board Diagnostics II
On-board Diagnostics (OBD2): A higher-layer protocol for encoding and decoding a vehicle's health parameters and engine values.
Parameters are read from the vehicles OBD2 connector port, usually located underneath the dashboard.
Used for emissions control, engine error diagnosis, predictive maintenance, and vehicle performance tracking.

## Slide 3: Examples of OBD2 Parameters
Possible fields for an OBD2 data frame include but are not limited to:
  Fuel Pressure: Pressure exerted on fuel as it moves through the fuel system of the engine.
  Engine Load: Determines the maximum load of the engine on a scale of 0 to 100%.
  Coolant Temperature: The temperature of the engine's coolant. Used to alter the fuel injection parameters and activate the cooling fan when needed.
  Engine RPM: Number of time the engine's crankshaft rotates in one minute.
  Oil Temperature: The temperature of the engine oil. Must be kept within a certain range for optimal performance depending on oil type.
  Oxygen Sensor Data: A measurement of the oxygen in the vehicle's exhaust. Used to ensure the engine is running optimally.

## Slide 4: The CAN Bus and CAN
CAN (Controller Area Network) is the standard for internal transmissions of data between a vehicle's ECUs (Electronic Control Unit).
CAN acts as a lower-level protocol for determining ECU to ECU (or node to node) communication. OBD2 acts as an upper-layer logical protocol.
CAN handles the transmission of CAN messages containing encapsulated OBD2 frames. OBD2 handles the encoding and decoding of OBD2 frames.
The data contained in the data field of a CAN message must be decoded using the decoding rules of the OBD2 protocol.

## Slide 5: Decoding CAN Data
The rules for decoding a CAN message's encoded data field are stored in a database file format called a DBC file.
DBC files contain the decoding rules for decoding hexadecimal values of a CAN message into the original physical engineering values (rpm, degC, etc).
The decoding rules for most of a vehicle's CAN bus communications are proprietary; decoding these messages is difficult.
Most communications used in OBD2 are standardized. Anyone with access can decode the diagnostic data from a vehicle's CAN bus.

## Slide 6: CAN Frame Structure
CAN frames follow a standardized format of ordered bits:
The most relevant fields are:
  ID: Used to determine the priority (lower-values take priority) and to identify the correct decoding rules to use from the DBC file.
  Data: Contains the encoded data (such as OBD2 physical values).

## Slide 7: DBC File Format
DBC files contain the decoding rules for CAN messages. Example:
The above fields each represent the rules for decoding a CAN message:
  BO_: Represents a CAN message identified by ID. Messages are composed of signals which each represent one physical value.
  SG_: Represents a possible signal. Located below the related message ID and are the rules for decoding a CAN message's physical values.

## Slide 8: DBC File Format (continued)
The structure for a CAN message's decoding rules in a DBC file are as follows:
The fields in a DBC file contain instructions for deriving the signal values.
A single DBC file may contain the decoding rules for many messages.

## Slide 9: OBD2 Frame Structure
OBD2 frames contain important metadata, such as the mode (or service) field, which are used to determine the correct signal decoding rules to use.
OBD2 frames contain important metadata, such as the mode (or service) field, which are used to determine the correct signal decoding rules to use.
The data bytes are contained in the four data byte fields, labelled A, B, C, and D.

## Slide 10: OBD2 Request
To get an OBD2 response message, an OBD2 request message must be sent.
Request example: 7DF 02 01 0C 00 00 00 00 00
7DF: The standard CAN ID for an OBD2 request.
02: The additional number of bytes of data used.
01: The service mode of the request (Show Current Data).
0C: The parameter ID of the value requested (Engine RPM).
00 00 00 00 00: Padding, which will be discarded.

## Slide 11: OBD2 Response
An OBD2 response message is sent in response to an OBD2 request message.
OBD2 response messages contain the requested physical values.
OBD2 response example: 7E8 04 41 0C 0B 1A 00 00 00
7E8: The standard CAN ID for an OBD2 response.
04: The additional number of bytes of data used.
41: Represents the service mode requested (Show Current Data).
0C: The parameter ID of the value requested (Engine RPM).
0B 1A: The encoded value of the requested data.
00 00 00: Padding, which will be discarded.

## Slide 12: OBD2 Future
OBD2 was originally developed to track emissions data for gas-powered vehicles.
As many vehicles move to being electrically powered, OBD2 is seeing a decline in adoption.
OBD2 may see competition, modification or reduction, or replacement.

## Slide 13: OBD2 Overview
OBD2 (On-board Diagnostics 2) is an upper-layer protocol for the Controller Area Network (CAN) for the encoding and decoding of engine health values.
Physical engine values are first encoded and transmitted in the data field of a CAN message, where it is read by any listening node or device.
To decode the data field, the decoding rules for the protocol must be obtained from a DBC file. OBD2 decoding rules are standardized.
Once decoded, the OBD2 physical values can be used for engine diagnostics, vehicle performance measurement, online telematics, or more.

## Slide 14: Additional Information
https://www.csselectronics.com/pages/can-bus-simple-intro-tutorial
https://www.csselectronics.com/pages/obd2-explained-simple-intro
https://www.csselectronics.com/pages/can-dbc-file-database-intro
https://en.wikipedia.org/wiki/On-board_diagnostics
https://en.wikipedia.org/wiki/CAN_bus
https://en.wikipedia.org/wiki/OBD-II_PIDs